Hellenic Accreditation System

Annex F1/9 to the Certificate No. 856-4 SCOPE of ACCREDITATION of the Laboratories in Metamorfosis Attiki of Laboratory Sewerage Analysis Department of Athens Water Supply & Sewerage Company S.A. (EYDAP S.A.)

| Tested materials/ products | Types of test/ Properties to be measured | Applied Methods/ Techniques to be used |
| --- | --- | --- |
| Chemical Testing |
| Industrial and domestic wastewater, wastewater treatment plant effluents, reuse water, surface water Industrial and domestic wastewater, wastewater treatment plant effluents, reuse water, surface water (cont’d) | 1. Determination of chemical oxygen demand (COD) | 1. MERCK 114540, 114541, 114691, 114555 2. HACH LCK 314, APC 314, LCK 514, APC 514, LCK 014, APC 014 |
|  | 2. Determination of the total suspended solids (TSS) | APHA(*) 2540 D |
|  | 3. Determination of total nitrogen | 1. MERCK 114537, 114763 |
|  | 4. Determination of total phosphorus | 1. MERCK 114729 |
|  | 5. Determination of orthophosphates | 1.MERCK 114729 |
|  | 6. Determination of hexavalent Cr | MERCK 114552 |
|  | 7. Determination of pH | APHA(*) 4500 - H+ B. |
|  | 8. Determination of color | MERCK 32 |
|  | 9. Determination of ammonium nitrogen | 1. MERCK 114739, 114544 |
|  | 10. Determination of ammonium | 1. MERCK 114739, 114544 |
|  | 11. Determination of nitrogen nitrates | 1. MERCK 114563 |
|  | 12. Determination of nitrates | 1. MERCK 114563 |
|  | 13. Determination of cyanide | MERCK 114561 |
| Microbiological Testing |
| Treatment Plant effluents | 1. Detection and enumeration of total coliforms and E.coli | EPA 1604:2002 |
|  | 2. Enumeration of fecal coliforms | APHA (*) 9222 D |

(*)APHA: Standard Methods for the Examination of Water and Wastewater, 23st Ed., 2017

Site of assessment :  Laboratory permanent premises, 13,5 Athens -Lamia Nat. Road, 14451 Metamorphosi, Attiki, Greece.

Approved signatories: D. Tsigalou, M. Psaroudi, Ch. Tourikas, E. Aidini.

This scope of Accreditation replaces the previous one dated 03.11.2021.

The Accreditation Certificate No. 856-4, to ΕLΟΤ EN ISO/IEC 17025:2017, is valid until 11.06.2024.

Athens, 03.08.2023

Christos Nestoras

CEO of ESYD