Hellenic Accreditation System

| Annex F2/11 to the Certificate No. 914-4 SCOPE of ACCREDITATION of the Volumetric Vessel and Meter Calibration Laboratory of PETROTEK S.A. |  |
| --- | --- |
| Measurand / Calibration item | Range of measurement | Calibration & Measurement Capability (k=2)* | Remarks |
| Volume measurements |
| Fixed storage tanks: - Cylindrical horizontal - Cylindrical vertical - Orthogonal of max height 3,5 m | [1 – 10] m3 | 0,10% | Volumetric method using volume meter according to ISO 4269: 2001. Calibration Εmedium: potable water. Calibration is performed on site. |
|  | (10 – 50] m3 | 0,07% |  |
|  | (50 – 100] m3 | 0,05% |  |
|  | (100 – 200] m3 | 0,04% |  |
| Road tankers | [1 – 10] m3 | 0,10% | Volumetric method using flow meter according to: - ISO 4269:2001 - OIML R 80-2: 2017 - Annex B Calibration medium: Tap water. Calibration is performed on site. |
|  | (10 – 50] m3 | 0,07% |  |
| Steel volumetric vessels of types “to contain” | 20 l – 500 l | 0,05% | Volumetric method using volumetric vessels according to EURAMET cg-21, v.2.0: 2020 Calibration medium: potable water. |

*Where uncertainty is accompanied by the corresponding unit, it is absolute, while where it is not accompanied by a unit, is relative.

Site of assessment: Permanent laboratory premises, Serron 15-17, 10441 Athens.

Approved Signatories:  A. Matagas, M. Kyriakopoulos.

This scope of Accreditation replaces the previous one dated 26.10.2022.

The Accreditation Certificate No. 914-4, to ELOT EN ISO/IEC 17025:2017, is valid until 12.05.2027.

Athens, 21.11.2022

Christos Nestoras

CEO of ESYD