Hellenic Accreditation System

Annex F2/8 to the Certificate No.983-3 SCOPE of ACCREDITATION οf the Calibration Laboratory CALIBRATION & TESTING GLOBETECH LABORATORIES S.A.

| Measurand / Calibration item | Range of measurement | Uncertainty* (Confidence level 95%) | Remarks |
| --- | --- | --- | --- |
| Force Measurements |
| Compression testing machines | [200 kN to 2000 kN] (2000 kN to 3000 kN] | 0,17 % 0,45 % | ISO 7500-1:2018 Class 1 machines. Calibration is performed on-site. |
| Compression testing machines: |  |  | ΕΝ 12390-4:2019 Calibration is performed on-site. |
| - Force transfer | Force ratio at applied force 200 kΝ to 3000 kN | 0,01 |  |
| - Force rate | 1 kN/s to 100 kN/s | 1% |  |
| - Flatness of machine plates | Go-NoGo 30 μm | 4,3 μm |  |
| - Hardness of machine plates | 27 HRC to 67 HRC | 2,3 HRC |  |
| - Roughness of machine plates | Ra: 0,4 μm to 3,2 μm | 0,032 μm to 0,12 μm |  |
| Torque wrenches | 3,5 Nm to 700 Nm | 0,6 % | ISO 6789-1:2017 ISO 6789-2:2017 using torque measurement system. |
| Dimensional Measurements |
| Calipers, analog / digital | 0 mm to 300 mm | 0,6 x d d: instrument division in μm d ≥ 10 μm | VDI 2618-9.1: 2006 |

* 	Where uncertainty is accompanied by the corresponding unit, it is absolute, while where it is not accompanied by a unit, it is relative.

Site of assessment: Permanent laboratory premises, Riga Fereou 11, 12462 Chaidari, Athens, Greece

Approved Signatories: M. Avraam, N. Stathatos, C. Geros.

This scope of Accreditation replaces the previous one dated June 2nd, 2023.

The Accreditation Certificate No. 983-3, to ELOT EN ISO/IEC 17025:2017, is valid until 07.06.2028.

Athens, July 7th, 2023

Christos Nestoras

CEO of ESYD