Hellenic Accreditation System

| Annex F2/2 to the Certificate No. 364-5 SCOPE of ACCREDITATION of the Calibration Laboratory BUREAU VERITAS HELLAS S.A. |
| --- |
| Measurand / Calibration item | Range of measurement | Uncertainty * (Confidence level 95%) | Remarks |
| Volume Measurements |
| Volume / Vertical cylindrical tanks | Up to 2500 m3 Maximum tank diameter 14 m | Height Diameter 1,2m 2,5 m 5 m >7,5 m 1 m 0,43% 0,23% 0,16% 0,14% >3 m - 0,22% 0,14% 0,12% on nominal tank volume | Calibration according to: ISO 7507-1:2003 (Strapping method) Bottom volume measurement: ISO 4269:2001, or ISO 7507-1:2003 (physical survey) |
|  | Up to 140000 m3 Minimum tank diameter 8 m | Height Diameter 3 m 8 m >12 m 8 m 0,17% 0,16% 0,15% 20 m 0,11% 0,09% 0,08% >50 m 0,09% 0,07% 0,05% on nominal tank volume | Calibration according to: ISO 7507-3:2006 (Optical triangulation method) Measurement - Calculation of Radius: ISO 7507-3:2006 (Optical triangulation method), or Measurement of Reference Circumference: ISO 7507-1: 2003 (Strapping method) Bottom volume measurement: ISO 4269:2001, or ISO 7507-1:2003 (physical survey) Volumetric table calculation and other measurements: ISO 7507-1:2003 |
|  | Up to 140000 m3 Minimum tank diameter 5 m | Height Diameter 4 m 10 m >15 m 5 m 0,15% 0,05% 0,04% >15 m 0,12% 0,05% 0,04% on nominal tank volume | Calibration according to: ISO 7507-4:2010 (Internal electro-optical distance-ranging method) Bottom volume measurement: ISO 4269:2001, or ISO 7507-1:2003 (physical survey) Volumetric table calculation and other measurements: ISO 7507-1:2003 |
| Measurand / Calibration item | Range of measurement | Uncertainty * (Confidence level 95%) | Remarks |
| Volume / Steel tanks | [5 – 10] m3 | 0,13% on nominal tank volume | Calibration according to: ISO 4269: 2001 Petroleum and liquid petroleum products – Tank calibration by liquid measurement – (Incremental method using volumetric meters) Volumetric method using flow meter Calibration medium: potable water Calibration can be performed on-site |
|  | (10 – 600] m3 | 0,085% on nominal tank volume |  |
| Volume / Horizontal cylindrical tanks | Up to 20000 m3 Minimum tank diameter 2 m | Length Diameter 5 m 10 m >20 m 2 m 0,18% 0,18% - 4 m 0,10% 0,10% 0,09% >12 m - - 0,03% on nominal tank volume | In-house electro-optical distance ranging method using 3D laser scanner, based on: ISO 12917-2:2002 (Internal electro-optical distance-ranging method) |
| Volume / Spherical tanks | Up to 10000 m3 Minimum tank radius 1,5 m | 0,04% on nominal tank volume | In-house electro-optical distance ranging method using 3D laser scanner, based on: API 2552:1965 (Method for measurement and calibration of spheres and spheroids) Internal and External calibration |
| Volume / Ship tanks | [10 – 120] m3 | 0,25% - 0,12% on nominal tank volume | In-house electro-optical distance ranging method using 3D laser scanner, based on: API MPMS Chapter2, Section 8A: 2007 (Calibration of Tanks on Ships and Oceangoing Barges) |
|  | (120 – 1500] m3 | 0,12% - 0,06% on nominal tank volume |  |
|  | (1500 – 30000] m3 | 0,06% on nominal tank volume |  |

* 	Where uncertainty is accompanied by the corresponding unit, it is absolute, while where it is not accompanied by a unit, it is relative.

Site of assessment: Permanent laboratory premises, 12th km Athens-Lamia National Road, 14452, Metamorfosi, Attiki, Greece

Approved Signatories:  D. Gerasimou

This Scope of Accreditation replaces the previous one dated 6.08.2019

The Accreditation Certificate No. 364-5, to ELOT EN ISO/IEC 17025:2017, is valid until 9.7.2023

Athens, 20.12.2019

Spyridon Podaras

CEO of ESYD