Hellenic Accreditation System

| Annex F2/9 to the Certificate No. 974-4 SCOPE of ACCREDITATION of the Tank Calibration Laboratory of Athanasios Mylonas |  |
| --- | --- |
| Calibration item / Parameters | Range of measurement | Expanded Measurement Uncertainty (k=2)* | Remarks |
| Liquid volume / Fixed metallic tanks | 0.5 m3 to 210 m3 | 0.1 % of nominal tank volume | Volumetric method through the use of a flow meter Calibration medium: Tap water Standard followed: ISO 4269: 2001 The calibration can be performed on site |
| Liquid volume / Road metallic tanks | 0,5 m3 to 40 m3 | 0.15 % of nominal tank volume | Volumetric method through the use of a flow meter Calibration medium: Tap water Standards followed: ISO 4269: 2001 OIML R80-2: 2017, Annex B The calibration can also be performed on site |

* Where the expanded uncertainty (with 95 % coverage) is accompanied by the corresponding unit, it is absolute, while where it is not accompanied by a unit, it is relative.

The Calibration Measurement Capability (CMC) includes the measured quantity, the measurement range and the measurement uncertainty, expressing the minimum measurement uncertainty which can be achieved in a calibration.

Permanent laboratory premises address: Agamemnonos str. 6, Dentropotamos, Thessaloniki.

Approved Signatories: A. Mylonas.

This Scope of Accreditation replaces the previous one dated 12.07.2023.

The Accreditation Certificate No. 974-4, to ELOT EN ISO/IEC 17025:2017, is valid until 21.04.2028.

Athens, 18.12.2023

Christos Nestoras

CEO of ESYD