Hellenic Accreditation System

| Annex F2/6 to the Certificate No. 1002-3 SCOPE of ACCREDITATION of the Calibration Laboratory of SKOPELITIS LEMONIS |
| --- |
| Calibration item / Parameters | Range of measurement | Expanded Measurement Uncertainty (k=2)* | Remarks |
| Volume measurements |
| Fixed metallic tanks | 1 m3 to 100 m3 | 0,1 % of nominal tank volume | Volumetric method Guideline followed: EURAMET cg-21 Version 2.1 (09/2021) Calibration medium: Tap water The calibration can be performed on site. |
| Road metallic tanks | 0,5 m3 to 40 m3 | 0,3 % of nominal tank volume | Volumetric method Calibration medium: Tap water Guidelines followed: EURAMET cg-21 Version 2.1 (09/2021) OIML R80-2: 2017, Annex B The calibration can also be performed on site |

* Where the expanded uncertainty (with 95 % coverage) is accompanied by the corresponding unit, it is absolute, while where it is not accompanied by a unit, it is relative.

The Calibration Measurement Capability (CMC) includes the measured quantity, the measurement range and the measurement uncertainty, expressing the minimum measurement uncertainty which can be achieved in a calibration.

Permanent laboratory premises address: 4th klm of National Road Volos-Larisa, 38 500, Volos, Greece.

Approved Signatory: L. Skopelitis, N. Skopelitis

This Scope of Accreditation replaces the previous one dated 15.09.2023.

The Accreditation Certificate No. 1002-3, to ELOT EN ISO/IEC 17025:2017, has been extended according to ESYD’s decision and it is valid until 04.07.2024.

Athens, 01.04.2024

Christos Nestoras

CEO of ESYD