Ηellenic Accreditation System

Annex F1/12 to the Certificate No. 658-3 SCOPE of ACCREDITATION of the Quality Control Laboratory of Supplies of Class III (fuels, lubricants, engine coolants) of the 873 Fuel Depot of the Ministry of National Defence

| Materials / Products to be tested | Types of test / Properties to be measured | Applied Methods / Techniques to be used |
| --- | --- | --- |
| Chemical tests |
| Used Lubricating oils and Hydraulic fluids | Determination of Wear Metals Al, Cr, Cu, Fe, Mg, Ni, Si, Ag, Na, Sn, Ti, Pb. | ASTM D 6595-17 Rotating Disc Electrode Atomic Emission Spectroscopy (RDE-AES). |
| Petroleum and products | Distillation of Petroleum Products at Atmospheric Pressure | ASTM D 86-17 |
|  | Determination of density (kg/m3) | ISO 12185:1996/Corr.1:2001 Oscillating U-tube method |
|  | Determination of sulfur content (mg/kg) | ISO 20846:2011 Ultraviolet fluorescence method |
|  | Determination of flash point (oC) | ASTM D93-16a Pensky-Martens closed cup method |
|  | Determination of vapor pressure (kPa) | ASTM D5191-15 |
|  | Determination of carbon residue | ISO 10370:2014 |
|  | Determination of cloud point (oC) | ASTM D5773-17e1 |
|  | Determination of pour point(oC) | ASTM D5949-16 |
| Petroleum | Determination of cold filter plugging point (oC) | ΕΝ 116:2015 |
| Aviation fuel | Determination of freezing point (oC) | ASTM D 5972-16 |
| Fuels - Lubricants | Determination of Dynamic Viscosity and Density of Liquids by Stabinger Viscometer (and the Calculation of Kinematic Viscosity) | ASTM D7042-16ε3 |

Site of assessment: Laboratory permanent premises, Kakiousi Military camp, End of 26th Octovriou str 54627 Thessaloniki, Greece.

Approved signatories: Major Paraskevas Paschalis, Sergeant Tsiakmakis Vasileios, Sergeant Zisou Nikolaos, Sergeant Karagianni Aikaterini, Sergeant Stougianni Eirini, Sergeant Dalkitsi Zoe, Sergeant Giouleka Ioanna, Established Official Oraiopoulos Lazaros.

This scope of Accreditation replaces the previous one dated 03.08.2022

The Accreditation Certificate No.658-3, to ELOT EN ISO/IEC 17025:2017, has been extended according to E.S.Y.D decision until 27.11.2022.

Athens, 15.11.2022

Christos Nestoras

CEO of E.SY.D.