Hellenic Accreditation System

Annex F1/13 to the Certificate No. 388-5 SCOPE of ACCREDITATION of the Laboratory of CHIMIKI TECHNIKI MINESCHOS L.P. for the performance of tests

| Materials/ Products to be tested | Types of test/ Properties to be measured | Applied methods/ Techniques to be used |
| --- | --- | --- |
| Performance tests |
| Visible and ultra-violet spectrophotometers (UV-Vis) | Wavelength accuracy (200 nm - 900 nm) | ASTM E 275: 2008 (R2022) Test is also performed on-site. |
|  | Stray light (220 nm) | ASTM E 387: 2004 (R2022) Test is also performed on-site. |
|  | Resolution (A268,7/A267,0) | NIST Special Publication 260-54 EurPharm 2.2.25 (11th ed./2024) Test is also performed on-site. |
| Visible and ultra-violet detectors (UV-Vis) of high-performance liquid chromatographs (HPLC) | Wavelength accuracy (240 nm - 650 nm) Linear range | ASTM E 1657: 1998 (2019) Test is also performed on-site. |
| Conductivity detectors of ion chromatographs (IC) and high-performance liquid chromatographs (HPLC) | Linear range | ASTM E 1511: 1993 (2017) The testing is also performed on site. |

Site of assessment: Permanent laboratory premises, 197, Spaton Avenue, GR-153 51 Pallini, Attiki, Greece.

Approved signatories: Gerasimos Mineschos.

This Scope of Accreditation replaces the previous one dated October 4th, 2023.

The Accreditation Certificate No. 388-5, to ELOT EN ISO/IEC 17025:2017, is valid until 09.10.2028.

Athens, March 15th, 2024

Christos Nestoras

CEO of E.SY.D