Hellenic Accreditation System

| Annex F2/7 to the Certificate No. 1107-3 SCOPE of ACCREDITATION of the Calibration Laboratory KOTSADAM PANAGIOTA – CALIBRATION SERVICES |
| --- |
| Calibration item / Parameters | Range of measurement | Expanded measurement uncertainty (k=2)* | Remarks |
| Volume Measurements |
| Volume / Vertical cylindrical tanks | Up to 12000 m3 Maximum tank diameter 28 m | Volume (m3) Uncertainty (%) 30 0,16 500 0,12 5000 0,11 12000 0,11 on nominal tank volume | Calibration according to ISO 7507-1:2003 Bottom volume measurement according to: ISO 4269:2001 ISO 7507-1:2003 (Physical Survey) Calibration is performed on-site. |
|  | Up to 150000 m3 Minimum tank diameter 8 m | Volume (m3) Uncertainty (%) 500 0,15 2000 0,09 10000 0,07 50000 0,06 100000 0,06 150000 0,05 on nominal tank volume | Calibration according to ISO 7507-3:2006 Measurement of reference circumference, volumetric table calculation and other measurements according to ISO 7507-1: 2003 Bottom volume measurement according to: ISO 4269:2001 ISO 7507-1:2003 (Physical Survey) Calibration is performed on-site. |
|  | Up to 10000 m3 Minimum tank diameter 8 m | Volume (m3) Uncertainty (%) 500 0,13 2000 0,09 10000 0,07 on nominal tank volume | In-house calibration method based on combination of ISO 7507-3:2006 and ISO 7507-1:2003 Measurement of reference circumference, volumetric table calculation and other measurements according to ISO 7507-1: 2003 Bottom volume measurement according to: ISO 4269:2001 ISO 7507-1:2003 (Physical Survey) Calibration is performed on-site. |
| Calibration item / Parameters | Range of measurement | Expanded measurement uncertainty (k=2)* | Remarks |
| Volume / Vertical cylindrical tanks (continued) | Up to 150000 m3 Minimum tank diameter 5 m | Volume (m3) Uncertainty (%) 500 0,12 2000 0,10 10000 0,06 50000 0,06 100000 0,06 150000 0,05 on nominal tank volume | Calibration according to ISO 7507-4:2010 Volumetric table calculation and other measurements according to ISO 7507-1: 2003 Bottom volume measurement according to: ISO 4269:2001 ISO 7507-1:2003 (Physical Survey) Calibration is performed on-site. |
| Volume / Horizontal cylindrical tanks | Up to 15.000 m3 | Volume (m3) Uncertainty (%) 50 0,11 100 0,11 500 0,11 2.500 0,12 7.500 0,05 15.000 0,05 on nominal tank volume | External calibration according to ISO 12917-1:2017 Calibration is performed on-site. |
|  | Up to 15.000 m3 Minimum tank diameter 2 m | Volume (m3) Uncertainty (%) 50 0,13 100 0,09 500 0,08 2.500 0,06 7.500 0,05 15.000 0,05 on nominal tank volume | Internal calibration according to ISO 12917-2: 2002 Calibration is performed on-site. |
| Volume / Spherical tanks | Up to 6.000 m3 | Volume (m3) Uncertainty (%) 200 0,35 500 0,22 2.000 0,12 6.000 0,07 on nominal tank volume | Calibration using strapping according to API 2552:1965 Calibration is performed on-site. |
|  |  | Volume (m3) Uncertainty (%) 200 0,38 500 0,24 2.000 0,12 6.000 0,08 on nominal tank volume | In-house electro-optical distance ranging method using total station, based on API 2552:1965 Calibration is performed on-site. |
| Calibration item / Parameters | Range of measurement | Expanded measurement uncertainty (k=2)* | Remarks |
| Volume / Fixed tanks | 0,5 m3 to 10 m3 | 0,11 % of nominal tank volume | Volumetric method using flow meter according to ISO 4269:2001 Calibration medium: Tap water Calibration is performed on site. |
|  | 10 m3 to 60 m3 | 0,10 % of nominal tank volume |  |
| Volume / Road tankers | 0,5 m3 to 10 m3 | 0,11 % of nominal tank volume | Volumetric method using flow meter according to: ISO 4269:2001 OIML R 80-2: 2017 - Annex B Calibration medium: Tap water Calibration is performed on site. |
|  | 10 m3 to 50 m3 | 0,10 % of nominal tank volume |  |

* 	Where the expanded uncertainty (with 95 % coverage) is accompanied by the corresponding unit, it is absolute, while where it is not accompanied by a unit, it is relative.

The Calibration Measurement Capability (CMC) includes the measured quantity, the measurement range and the measurement uncertainty, expressing the minimum measurement uncertainty which can be achieved in a calibration.

Permanent laboratory premises address: Anemonon 14, Alimos 17456, Attiki, Greece

Road tank calibration site, 3 km Isthmos - Epidaurus, Isthmia Korinthias 20150

Approved Signatories:  N. Tsalamandris

This Scope of Accreditation replaces the previous one dated 23.05.2022.

The Accreditation Certificate No. 1107-3, to ELOT EN ISO/IEC 17025:2017, is valid until 19.11.2025.

Athens, 01.08.2023

Christos Nestoras

CEO of ESYD