Hellenic Accreditation System

Annex F2/7 to the Certificate No. 141-4 SCOPE of ACCREDITATION of the Dimensional Metrology and Calibration Laboratory of Hellenic Defense Systems S.A.

| Measurand / Calibration item | Range of measurement | Calibration & Measurement Capability (k=2)* | Remarks |
| --- | --- | --- | --- |
| Dimensional measurements |
| Gauge blocks made of steel, category 0, 1, 2 | (0,5≤ln≤10) mm | 0,088 μm | Calibration using mechanical comparator according to ELOT ΕΝ ISO 3650 : 1998 |
|  | (10<ln≤25) mm | 0,091 μm |  |
|  | (25<ln≤50) mm | 0,098 μm |  |
|  | (50<ln≤75) mm | 0,110 μm |  |
|  | (75<ln≤100) mm | 0,124 μm |  |
| Internal distance between parallel surfaces | (5 - 150) mm | 2,21 μm | Gauge block slip calibration. |
| External diameter of plug / ring | D≤300 mm | 0,87 μm | Calibration using machine SIP -302 M |
| Internal diameter of ring | (10 – 205) mm | 1,04 μm | Calibration using machine SIP -302 M |
| Equivalent and basic diameter of external thread of plug / ring | M1 – M150 | 2,84 μm | Calibration using machine SIP -302 M |
| Thread external diameter of plug / ring | Diameter up to 250 mm | 2,84 μm | Calibration using machine SIP -302 M |
| External axial micrometers: | Calibration using standard gauge blocks of category 1 |
| Α. Digital / division 1 μm | (0 – 100) mm | 1,48 μm |  |
| Β. Analog / division 1 μm | (0 – 100) mm | 1,47 μm |  |
| C. Analog / division 10 μm | (0 – 50) mm | 3,32 μm |  |
|  | (50 – 100) mm | 3,39μm |  |
| Calipers: |  |  | Calibration using step gauge blocks (Cera caliper) and standard gauge blocks of category 1 |
| A. Digital / division 10 μm | (0 – 150) mm | 5,94 μm |  |
| B. Analog / division 20 μm | (0 – 150) mm | 6,56 μm |  |
| C. Analog / division 50 μm | (0 – 150) mm | 16,38 μm |  |
| Dial gauges: | Calibration using machine TRIMOS THV (comparing the dial gauge with the dial of HEIDENHEIN) |
| Α. Lever / division 10 μm division 2 μm | 0,5 / 0,8 / 1,6 mm 0,2 / 0,24 mm | 2,90 μm 0,60 μm |  |
| Β. Plunger / division 10 μm | 3 / 5 / 10 mm | 2,91 μm |  |

* Where uncertainty is accompanied by the corresponding unit, it is absolute, while where it is not accompanied by a unit, it is relative.

Site of assessment:  Permanent laboratory premises, Ilioupoleos Ave 1, Imittos, Attiki, Greece.

Approved Signatories: A. Ntokas, P. Tsakonas.

This Scope of Accreditation replaces the previous one dated 10.01.2013.

The Accreditation Certificate No. 141-4, to ELOT EN ISO/IEC 17025:2005, has been extended up to 15.09.2019.

Athens, 12th May 2016

Ioannis Sitaras

Director of the Laboratories Accreditation Division