Hellenic Accreditation System

| Annex F1/17 to the Certificate No. 566-5 SCOPE of ACCREDITATION of the Chemical Laboratory of the Hellenic Petroleum R.S.S.O.P.P. S.A., Elefsis Industrial Plant |
| --- |
| Materials / Products to be tested | Types of tests / Properties to be measured | Applied methods / Techniques to be used |
| Physicοchemical Tests |
| 1. Petroleum products | 1.Determination of density | Oscillating U-tube method ELOT ΕΝ ISO 12185:1996 (R2020), ASTM D 4052- 2022 |
|  | 2.Determination of Density | Hydrometer method ISO 3675: 1998 (R2020), ASTM D 1298: 2012b (2017) |
|  | 3.Determination of flash point | Α. Closed cup method Pensky Martens EN ISO 2719:2016/A1:2021, ASTM D 93: 2020 |
|  |  | Β. Flash Point by Tag closed cup tester ASTM D56:2022 |
|  | 4. Freezing Point of Aviation Fuels | ASTM D7153:2022a, IP529:2016, (Automatic Laser Method) |
|  | 5.Determination of cold filter plugging point | Method of determination of cold filter plugging point EN 116:2015 IP 309:2016 |
|  | 6. Determination of sulfur content | Ultraviolet fluorescence method EN ISO 20846: 2019, ASTM D 5453: 2019a |
|  | 7. Distillation of Petroleum Products at Reduced Pressure | Distillation at reduced pressure ASTM D1160-2018 |
| Materials / Products to be tested | Types of test / Properties to be measured | Applied methods / Techniques to be used |
|  | 8. Determination of thermal oxidation stability of aviation fuels | ASTM D3241:2020c IP 323 (reap. 2022) |
|  | 9. Determination of Aromatic Hydrocarbon Types—High Performance Liquid Chromatography Method with Refractive Index Detection | ASTM D6379-21e1 IP 436: 2020 |
|  | 10. Determination of the fatty acid methyl esters content of aviation turbine fuel using flow analysis by Fourier transform infrared spectroscopy | ASTM D-7797-23, IP 583-15 (R2021) |
| 2. Fuel and Refinery gases | 1.Determination of the composition of fuel and refinery gases | Gas Chromatography method *UOP 539: 2012 |

* UOP: Universal Oil Products, Laboratory Test Methods for Petroleum and its Products

Site of assessment:  Permanent laboratory premises, 27th km. Old Athens – Corinth National Road, Elefsina, Attiki, Greece.

Approved Signatories: S. Kiriakou, K. Flessas, M. Kamaterou, Em. Lymperis.

This Scope of Accreditation replaces the previous one dated 28.11.2022.

The Accreditation Certificate No. 566-5, to ELOT EN ISO/IEC 17025:2017, is valid until 02.06.2025.

Athens, 19.09.2023

Christos Nestoras

CEO of ESYD