Hellenic Accreditation System

| Annex F2/2 to the Certificate No. 1263 SCOPE of ACCREDITATION of the Calibration Laboratory ROPI P.C. |
| --- |
| Calibration item / Parameters | Range of measurement | Expanded measurement uncertainty (k=2) * | Remarks |
| Volume Measurements |
| Vertical cylindrical fuel tanks | Up to 4000 m3 Maximum tank diameter 20m | Volume Uncertainty 35 m3 0,20 % 500 m3 0,15 % 4000 m3 0,11 % on nominal tank volume | Calibration according to: ISO 7507-1:2003 (strapping method) Bottom volume measurement: ISO 7507-1:2003 (physical survey) |
|  | Up to 140000 m3 Minimum tank diameter 8 m | Height Diameter 3,6 m 9 m > 14,5m 8 m 0,18 % 0,14 % 0,12 % 20 m 0,11 % 0,09 % 0,08 % > 60 m 0,07 % 0,06 % 0,06 % on nominal tank volume | Calibration according to: ISO 7507-3:2006 (optical triangulation method) Measurement - calculation of radius: ISO 7507-3:2006 (optical triangulation method) with measurement of reference circumference: ISO 7507-1: 2003 (strapping method) Bottom volume measurement: ISO 7507-1:2003 (physical survey) Volumetric table calculation and other measurements: ISO 7507-1:2003 |
| Calibration item / Parameters | Range of measurement | Expanded measurement uncertainty (k=2) * | Remarks |
| Vertical cylindrical fuel tanks (continued) | Up to 140000 m3 Minimum tank diameter 5 m | Height Diameter 3,6 m 9 m > 14,5 m 5 m 0,15 % 0,12 % 0,11 % 20 m 0,08 % 0,07 % 0,06 % > 60 m 0,06 % 0,06 % 0,06 % on nominal tank volume | Calibration according to: ISO 7507-4:2010 (internal electro-optical distance-ranging method) Bottom volume measurement: ISO 7507-1:2003 (physical survey) Volumetric table calculation and other measurements: ISO 7507-1:2003 |

*	Where the expanded uncertainty (with coverage probability 95 %) is accompanied by the corresponding unit, it is absolute, while where it is not accompanied by a unit, it is relative.

The Calibration & Measurement Capability (CMC) includes the measurand, the measurement range and the measurement uncertainty and expresses the smallest measurement uncertainty that can be achieved in a calibration.

Permanent laboratory premises address: Nikitara 21, 54628 Menemeni, Thessaloniki, Greece

Approved Signatories:  Ch. Bolmatis, M. Bolmati

This Scope of Accreditation replaces the previous one dated 06.08.2021.

The Accreditation Certificate No. 1263, to ELOT EN ISO/IEC 17025:2017, is valid until 05.08.2025.

Athens, 18.09.2023

Christos Nestoras

CEO of ESYD