Hellenic Accreditation System

Annex F1/A23 to the Certificate No. 192-7 SCOPE of ACCREDITATION of the Laboratory at Galatsi of the Water Quality Control Department of the Planning and Supporting Operations for Water Sector Division of the Athens Water Supply & Sewerage Company S.A. (EYDAP)

| Tested materials/ products | Types of test/ Properties to be measured | Applied Standards/ Techniques to be used |
| --- | --- | --- |
| Chemical Tests |
| Drinking water, surface water, brackish water and sea water. | 1.Determination of conductivity | Method 2510 Β (APHA, Standard Methods 24th ed., 2023) |
|  | 2.Determination of nitrite | Ιn-house method (O504_10_31) based on APHA 4500 NO2, Β, Standard Methods 24th ed., 2023 (discrete analysis with photometric detection) |
| Drinking water | Determination of free chlorine | Ιn-house method (O504_10_48) based on APHA 4500-Cl G 24th ed., 2023) and on ISO 7393-2:2017 |
| Drinking water and surface water | 1.Detrmination of pH | Method 4500-Η, Β (APHA, Standard Methods 24th ed., 2023) |
|  | 2.Determination of turbidity | Method 2130 Β (APHA, Standard Methods 24th ed., 2023) |
|  | 3.Determination of aluminium | Ιn-house method (O504_10_32) based on APHA 3500-Al, B, Standard Methods 24th ed., 2023 (discrete analysis with photometric detection) |
|  | 4.Determination of fluoride | Ιn-house method (O504_10_45) based on ISO/TS 15923-2:2017 (discrete analysis with photometric detection) |
|  | 5.Determination of chloride | Method ISO 15923-1:2013 (discrete analysis with photometric detection) |

| Tested materials/ products | Types of test/ Properties to be measured | Applied Standards/ Techniques to be used |
| --- | --- | --- |
| Drinking water and surface water. (continued) | 6. Determination of bromide, chlorite and chlorate | Ιn-house method (O504_10_14) based on APHA 4110 Β and D (Standard Methods 24th ed., 2023) (Ion-chromatography method) |
|  | 7. Determination of nitrate | Ιn-house method (O504_10_38) based on ISO 15923-1:2013 (discrete analysis with photometric detection) |
|  | 8. Determination of orthophosphate | Ιn-house method (O504_10_40) based on ISO 15923-1:2013 (discrete analysis with photometric detection) |
|  | 9. Determination of sulphate | Ιn-house method (O504_10_41) based on ISO 15923-1:2013 (discrete analysis with photometric detection) |
|  | 10. Determination of total alkalinity | Ιn-house method (O504_10_35) based on Methods for the Examination of Waters and Associated Materials. The determination of Alkalinity and Acidity in Water 1981 (discrete analysis with photometric detection) |
|  | 11. Determination of calcium ions | Method ISO/TS 15923-2:2017 (discrete analysis with photometric detection) |
|  | 12. Determination of magnesium ions | Method ISO/TS 15923-2:2017 (discrete analysis with photometric detection) |
|  | 13. Determination of color | Ιn-house method (O504_10_34) based on APHA 2120 Color C, Standard Methods 24th ed., 2023 (discrete analysis with photometric detection) |
|  | 14. Determination of ammonium | Ιn-house method (O504_10_33) based on ISO 15923-1:2013 (discrete analysis with photometric detection) |
|  | 15. Determination of hardness | Ιn-house method (O504_10_20) based on APHA 2340 B Hardness by calculation, Standard Methods 24th ed., 2023 (discrete analysis with photometric detection) |
|  | 16. Determination of cyanide | Ιn-house method (O504_10_53) based on HACH APP-PHM-0007 |
| Microbiological Tests |
| Drinking water Drinking water (continued) | 1.Εnumeration of Escherichia coli and coliform bacteria | ISO 9308-1 : 2014 |
|  | 2.Εnumeration of Escherichia coli and coliform bacteria | ISO 9308-2 : 2012 |
|  | 3.Detection and enumeration of intestinal enterococci | ISO 7899-2 : 2000 |
|  | 4.Εnumeration of Clostridium perfringens, (spores included) | ISO 14189 : 2013 |
|  | 5.Enumeration of culturable microorganisms at 36 οC and 22 oC | ISO 6222:1999 |
| Drinking water and surface water | Detection of Salmonella spp | ISO 19250: 2010 |
| Surface water | Detection and enumeration of enterococci | Method 9230D (APHA, Standard Methods 24th ed.,2023) |
| Sensory tests |
| Drinking Water of EYDAP’s water distribution network | Taste & Odor – Qualitative simplified procedures | ΕΝ 1622:2006-ΑΝΝΕΧ C |
| Sampling |
| Drinking water | Sampling for microbiological and chemical tests | Standard Methods for the Examination of Water and Wastewater, (24th ed) ISO5667-1:2020 ISO5667-3:2018 ISO5667-4:2016 ISO5667-5:2006 ISO5667-6:2014 ISO5667-11:2009 ISO5667-14:2014 ISO19458:2006 |

Site of assessment :  Laboratory of Galatsi permanent premises, 156 Oropou str., Galatsi, Attiki.

Approved signatories: D. Tsorova, A. Kagiara, T. Kaloudis, E. Farmaki, A. Gialleli, N. Deftereos.

This Scope of Accreditation replaces the previous one dated 15.06.2023.

The Accreditation Certificate No 192-7, to ΕLΟΤ ISO/IEC 17025:2017, is valid until 10.01.2025.

Athens, 29.02.2024

Christos Nestoras

CEO of EYD

Hellenic Accreditation System

Annex F1/B18 to the Certificate No. 192-7 SCOPE of ACCREDITATION of the Laboratory at Acharnes of the Water Quality Control Department of the Planning and Supporting Operations for Water Sector Division of the Athens Water Supply & Sewerage Company S.A. (EYDAP)

| Tested materials/ products | Types of test/ Properties to be measured | Applied Standards/ Techniques to be used |
| --- | --- | --- |
| Chemical Tests |
| Drinking water and surface water | Determination of metals: Cd, Cr, Cu, Fe, Mn, Ni, B, K, Na | ISO 11885:2007 |
| Drinking water | 1.Determination of Trihalomethanes (THM) and Volatile Organic Compounds (VOC): THM: chloroform, bromoform, dibromochloromethane, bromodichloromethane, total trihalomethanes. b)VOC: benzene, 1,2-dichloroethane, tetrachoroethene and trichloroethene, bromochloromethane, dibromomethane, toluene, 1,2-dibromoethane, chlorobenzene, styrene, bromobenzene, n-butyl benzene, hexachlorobutadiene, naphthalene, 1,1-dichloroethane, 1,1-dichloroethene, 1,1,2-trichloroethane, 1,1,2,2-tetrachloroethane, 1,2-dibromo-3-chloropropane, 1,2-dichloropropane, 1,2,3-trichlorobenzene, 1,2,4-trichlorobenzene, 1,3-dichloropropane, ethylbenzene, n-propylbenzene, o-xylene, p+m-xylenes, sec-butylbenzene, tert-butylbenzene | ΕLΟΤ ΕΝ ΙSΟ 17943:2016 (HS-SPME-GC/MS) |
| Drinking water (continued) | 2.Determination of Total Organic Carbon (TOC) | In-house method (Ο510_4_45) based on ISO/DIS 20236:2018 and ΕLΟΤ EN 1484:1997 |
|  | 3. Determination of geosmin and 2-methylisoborneol | In-house method, HS-SPME-GC-MS/MS or HS-SPME-GC-MS (O504_10_49) |
|  | 4. Determination of microcystins and cyanopeptides: Anabaenopeptin A, Anabaenopeptin B, Microcystin-LA, Microcystin-LF, Microcystin-LR, Microcystin-LW, Microcystin-LY, Microcystin-RR, Microcystin-YR, Microcystin-HtyR, Nodularin | In house method (Ο510_4_55) using LC-qTOF based on ISO 22104:2021 |
|  | 5. Determination of pesticides residues: Carbofuran, Cycluron, Diethofencarb, Dimethomorph, Diuron, Fenhexamid Fenoxycarb, Fenuron, Fluometuron, Isoprocarb, Isoproturon, Linuron, Methomyl, Metobromuron, Monolinuron Myclobutanil, Neburon, Piperonyl butoxide, Pirimicarb, Promecarb, Siduron, Triflumuron | In-house method (Ο510_4_56) using LC-qTOF (TargetScreener method, Bruker) |
| Surface water | Determination of Dissolved Organic Carbon (DOC) | In-house method (Ο510_4_45) based on ISO/DIS 20236:2018 and ΕLΟΤ EN 1484:1997 |

Site of assessment :  Laboratory of Acharnes permanent premises, Acharnes, Attiki.

Approved signatories: E. Farmaki, T. Kaloudis, A. Gialleli, N. Deftereos

This Scope of Accreditation replaces the previous one dated 15.06.2023.

The Accreditation Certificate No 192-7, to ΕLΟΤ ΕΝ ISO/IEC 17025:2017, is valid until 10.01.2025.

Athens, 29.02.2024

Christos Nestoras

CEO of ESYD