Hellenic Accreditation System

Annex F1/12 to the Certificate No. 504-6 SCOPE of ACCREDITATION of the Testing Laboratory Food Quality Control Laboratory Stellakis D. Alexios (Stel.Lab)

| Materials/Products tested | Types of test/Properties measured | Applied methods/Techniques used |
| --- | --- | --- |
| Chemical Testing |
| 1. Milk | Determination of freezing point | Thermistor cryoscope routine method ISO 5764:2009 |
| 2. Vegetable oils | 1. Determination of free fatty acids, cold method | Commission Regulation (EEC) No. 2022/2105, annex II, as in force |
|  | 2. Spectrophotometric investigation in the ultraviolet | Commission Regulation (EEC) No. 2022/2105, annex II, as in force |
| Microbiological Tests |
| 1.Foodstuffs and animal feeding stuffs | 1. Detection of Salmonella spp. (not included Salmonella Typhi and Salmonella Paratyphi) | ISO 6579-1:2017/Amd 1:2020 |
|  | 2. Detection of Listeria monocytogenes | AFNOR BKR 23/02-11/02 |
|  | 3. Enumeration of coagulase positive staphylococcus | ISO 6888-2:2021/Amd 1:2023 |
|  | 4. Enumeration of β-glucoronidase positive Escherichia coli | ISO 16649-2:2001 |
| 2.Animal faeces and environmental samples from the primary production stage | 1. Detection of Salmonella spp. (not included Salmonella Typhi and Salmonella Paratyphi) | ISO 6579-1:2017/Amd 1:2020 |
| 3. Milk | Bacteria enumeration | In house procedure (M19) using Foss Bactoscan FC+ based on manufacturers’ recommended method |
|  | Detection of antimicrobial residues [Betalactams, Tetracyclines] | Μέθοδος διάχυσης κατασκευαστή Symmetric B+T |

Site of assessement: Permanent Laboratory premises, Mountzouropoulou 75, Tripoli.

Approved signatories: Al. Stellakis.

This Scope of Accreditation replaces the previous one dated 07.06.2022.

The Accreditation Certificate No. 504-6, to ELOT EN ISO/IEC 17025:2017, is valid until 10.02.2025.

                - Athens, 09.01.2024

Christos Nestoras

CEO of ESYD