Hellenic Accreditation System

Annex F2/15 to the Certificate No. 647-4 SCOPE of ACCREDITATION of the Laboratory for Wind Turbine Testing of the Centre for Renewable Energy Sources and Saving (CRES) for the performance of calibrations

| Measurand / Calibration item | Range of measurement | Calibration & Measurement Capability (k=2)* | Remarks |
| --- | --- | --- | --- |
| Air Speed Measurements |
| Wind Speed / Cup anemometers Ultrasonic anemometers Propeller anemometers Hot-wire anemometers | 4 m/s … 16 m/s | 0,10 m/s | IEC 61400-12-1: 2017 (ANNEX F) MEASNET Anemometer calibr. Ver.3/2020 Internal Method CLP-03 |
| Wind direction / Wind vanes Ultrasonic anemometers | 0-360deg | 1.17 deg | IEC 61400-12-1:2017 (ANNEX N) |

* Where uncertainty is accompanied by the corresponding unit, it is absolute, while where it is not accompanied by a unit, it is relative.

Site of assessment: Permanent laboratory premises, 19th km Marathonos Ave., GR-190 09 Pikermi, Attiki, Greece.

Approved Signatories: N. Stefanatos, A. Kostakos, N. Drougas, D. Theofilogiannakos, F. Kokkalidis, P. Papadopoulos.

This Scope of Accreditation replaces the previous one dated 22.06.2022.

The Accreditation Certificate No. 647-4, to ELOT EN ISO/IEC 17025:2017, has been extended upon ESYD’s decision until 29.12.2022.

Athens,  26.09.2022

Christos Nestoras

CEO of ESYD