Hellenic Accreditation System

Annex F2/10 to the Certificate No. 751-5 SCOPE of ACCREDITATION of the Measurements and Calibration Laboratory of ESTIA CONSULTING AND ENGINEERING S.A. for the performance of calibrations

| Calibration item / Parameters | Range of measurement | Expanded Measurement Uncertainty (k=2) | Remarks |
| --- | --- | --- | --- |
| Air speed measurements |
| Air speed / cup anemometers | 4 m/s to16 m/s | 0,10 m/s | In-house method TDNC-07 based on: IEC 61400-50-1:2022, par.8 |
| Wind direction measurements |
| Wind direction / Wind direction sensors: - Potentiometric sensors with voltage measurement | 0o to 360o | 1,2° | IEC 61400-50-1:2022 ANNEX A Calibration is performed in an open circuit wind tunnel |

Site of assessment:  1st km. Thermi - “Makedonia” Airport Road, GR-570 01 Thermi - Thessaloniki, Greece.

Permanent calibration laboratory premises: Palaia Symmachiki Odos Diavaton Oraiokastrou (Behind Anagnostopoulou Camp) – GR-570 08 Ionia, Thessaloniki, Greece.

Approved signatories: Gkliagias Dimitrios, Katsanevaki Eleni, Romanidis Charalambos, Tifkitsis Konstantinos,Konstantinos Souleimanis.

This Scope of Accreditation replaces the previous one dated 03.01.2024.

The Accreditation Certificate No.751-5, to ELOT EN ISO/IEC 17025:2017, is valid until 19.06.2028.

Athens, 09.01.2024

# Christos Nestoras

CEO of ESYD