Hellenic Accreditation System

Annex F1/22 to the Certificate No. 158-7 SCOPE of ACCREDITATION of the Chemical Laboratories of Aspropyrgos Refinery of the Hellenic Petroleum R.S.S.O.P.P. S.A.

| Materials / Products to be tested | Types of test / Properties to be measured | Applied methods / Techniques to be used |
| --- | --- | --- |
| Chemical tests |
| 1. Unleaded gasoline, unleaded gasoline 98 RON, unleaded gasoline 100 RON | Determination of the benzene content by infrared spectrometry | ELOT ΕΝ 238:1996 & ELOT EN 238/A1:2004 |
| 2. Unleaded gasoline, unleaded gasoline 98 RON, unleaded gasoline 100 RON, jet A-1 & JP-8, diesel fuel, heating petrol, marine distillate fuel, army diesel, navy gasoil | Determination of density of petroleum products by the digital density meter-Oscillating U-tube method | ELOT ΕΝ ISO 12185:1996 ASTM D 4052:2022 |
| 3. Fuel oil Νο. 1 & 3, diesel fuel, heating petrol, marine distillate fuel, army diesel, navy gasoil, marine residual fuel | Determination of flash-point by Pensky-Martens closed cup tester | ΕLΟΤ ΕΝ ISO 2719:2016 ASTM D 93:2020 |
| 4. Marine residual fuel, fuel oil No. 1 & 3 | Determination of carbon residue (Micro method) | ΕLΟΤ ΕΝ ISO 10370:2014 ASTM D 4530:2020 |
| 5. Diesel fuel, Army diesel | Determination of polyaromatic hydrocarbons in diesel by HPLC | *IP 391:2019 ELOT EN 12916:2019 |
| 6. Diesel fuel, Army diesel | Assessment of lubricity in diesel fuel | ΕΛΟΤ EN ISO 12156-1:2023 |
| 7. Marine residual fuel, fuel oil No. 1 & 3, fuel oil for internal use | Determination of density by the hydrometer method | ISO 3675:1998 ASTM D 1298: 2017e1 |
| 8. Refinery gas | Refinery gas analysis by gas chromatography | **UOP 539:2012 |
| 9. Kerosene and jet A-1 | Determination of freezing point of aviation fuels (automatic phase transition method) | ASTM D 5972:2023 |
| 10. Κerosene, jet A-1 and JP-8 | Determination of aromatic hydrocarbon types in aviation fuels by the HPLC-RID method | ASTM D 6379:2021 e1 |
| 11. Unleaded gasolines | Determination of benzene, aromatic hydrocarbon types, olefins, ΜΤΒΕ, ETBE, ΤΑEΕ and total oxygen by multidimensional gas chromatography method | ASTM D 6839-2021 a. ΕLΟΤ EN ISO 22854:2021 |
| 12. Diesel fuel, army diesel, navy gasoil | Determination of cold filter plugging point (CFPP) | ΕΝ 116:2015, ASTM D 6371-2017a |
| 13. JET A-1, JP8 | Determination of Flash Point by Tag Closed Cup Tester | ASTM D56:2022 |
| 14. Unleaded Gasoline | Determination of air saturated vapour pressure (ASVP) and calculated dry vapour pressure equivalent (DVPE). | ELΟΤ ΕΝ 13016-1 Ε3:2018 |
| 15. Κerosene, JET A-1 and JP8 | Determination of freezing point of aviation fuels (automatic laser method) | ASTM D 7153:2022 |

*IP: Energy Institute (in the past Institute of Petroleum), Standard Methods for Analysis and Testing of Petroleum and Related Products

** UOP: Universal Oil Products, Laboratory Test Methods for Petroleum and its Products

Site of assessment: Laboratory Permanent premises, Aspropyrgos Refinery, 17th km. of the Athens-Corinth National Road, Greece.

Approved signatories: V. Tatsis, A. Trimpalis, D. Tiganitis, M. Giannia, E.Vasileiou, V. Vousoura.

This Scope of Accreditation replaces the previous one dated 01.11.2023.

The Accreditation Certificate No. 158-7, to ELOT EN ISO/IEC 17025:2017, is valid until 19.04.2029.

Athens, 23.04.2024

Christos Nestoras

CEO of ESYD